## Slide 1
Modernizing Water Resource Management: FIRO at Lake Oroville
Evan Spanner | WR 440 Capstone Project | Colorado State University | Spring 2026
FORECAST-INFORMED RESERVOIR OPERATIONS
CLIMATE ADAPTATION
CALIFORNIA WATER POLICY

## Slide 2
THE PROBLEM
Static Rules in a Changing Climate
Outdated Infrastructure
Static rules govern systems facing fundamentally different conditions today
Atmospheric River Risk
ARs cause over 90% of flood damages in the western U.S. — and are projected to intensify
Science-Practice Gap
Better tools already exist. The gap between science and operational practice keeps widening

## Slide 3
RESEARCH QUESTION
Can Reservoir Rules Keep Pace with Climate?
"What does effective water resource management look like in an era of increasing climate variability, and how can reservoir operating rules better serve that goal?"
01
Analyze Operations
Existing reservoir inflow and outflow patterns
02
Identify Optimal Thresholds
Balance flood control, water supply, and aquifer recharge
03
Compare Scenarios
Downstream discharge — before and after FIRO
04
Infer Downstream Impacts
Effects on downstream users under forecast-informed operations

## Slide 4
STUDY AREA
Lake Oroville & the Feather River Watershed
[Figure 1 — Study Area Map]
Insert Fig 1 here: Watershed map showing Lake Oroville, Feather River, and Yuba City / Marysville downstream constraint point.
Lake Oroville
Largest reservoir in the CA State Water Project
Oroville Dam
Tallest dam in the U.S. — 770 ft
Feather River Watershed
3,607 sq mi drainage area
Downstream Constraint
150,000 CFS channel capacity at Yuba City / Marysville

## Slide 5
HISTORICAL OPERATIONS
56 Years of High-Flow Events
[Figure 2 — Event Timeline]
Insert Fig 2 here: Timeline of 44 high-flow events (1970–2026) highlighting 1986, 1997, and 2017 major floods.
56
Year Record
1970 – 2026
44
High-Flow Events
Exceeding 15,000 CFS threshold
3
Major Floods
1986 · 1997 · 2017

## Slide 6
CURRENT RULES
The 1970 Water Control Manual
What It Does
Static guide curve tied to wetness index (WI 3.5 – 11+)
Max flood reservation: 750,000 AF at WI = 11 (elev. 848.5 ft)
Release schedule keyed to inflow magnitude only
What It Cannot Do
Pre-release ahead of incoming storms
Scale response to predicted severity
Incorporate any forecast information
Unchanged for 55+ years — no forecast input by design

## Slide 7
THE SOLUTION
Forecast-Informed Reservoir Operations (FIRO)
FIRO replaces static rules with forecast-responsive flood pool management — using weather intelligence to make smarter release decisions before storms arrive.
Dynamic Flood Pool
600K AF (1-in-5 yr) → 750K AF (1-in-25 yr) → 925K AF (1-in-100 yr)
Tiered Release Ceilings
30K → 60K → 100K → 150K CFS scaled by Annual Exceedance Probability
Pre-Event Drawdown
Key mechanism — create storage before the storm, not during it
Precedent: Lake Mendocino FIRO implemented 2020 · Rules source: Yuba-Feather FVA (2025)

## Slide 8
METHODS
Simulation Framework
Build Simulator
Daily mass-balance Python model, 56-year record
Compare Results
Three case events and full period-of-record analysis
Run Scenarios
Baseline WCM vs FIRO ID3A with identical inflows
Two Scenarios — Same Inputs
Baseline
1970 WCM rules applied mechanically across full record
FIRO Alternative
ID3A prescriptive rules from the Yuba-Feather FVA (2025)
Perfect-foresight forecast used — represents upper bound on FIRO performance

## Slide 9
CASE STUDY 1
February 1986
[Figure 3 — 1986 Event Hydrograph with AR Overlay]
Insert Fig 3 here: Hydrograph comparing WCM vs. FIRO outflows during Feb 1986 atmospheric river event.
WCM Peak Release
100,000 CFS
FIRO Peak Release
60,000 CFS — 40% reduction
Peak Elevation
861.4 ft (WCM) vs 900.4 ft (FIRO)

## Slide 10
CASE STUDY 2
January 1997 — Most Severe on Record
[Figure 4 — 1997 Event Hydrograph with AR Overlay]
Insert Fig 4 here: Hydrograph comparing WCM vs. FIRO outflows during Jan 1997 event (317,234 CFS full natural flow).
Full Natural Flow
317,234 CFS — record inflow
WCM Peak Release
150,000 CFS — full design discharge
FIRO Peak Release
124,582 CFS — 16.9% reduction, stayed within channel capacity

## Slide 11
CASE STUDY 3
February 2017 — The Boundary Case
[Figure 5 — 2017 Event Hydrograph with AR Overlay]
Insert Fig 5 here: Hydrograph for Feb 2017 showing dual-pulse storm pattern and 100,000 CFS peak for both scenarios.
Key Findings
Spillway failure — 188,000 evacuated
Both scenarios peaked at 100,000 CFS — zero net reduction
Two storm pulses separated by one week limited forecast advantage
Boundary case for a 5-day forecast rule — FIRO cannot overcome all storm patterns

## Slide 12
PERIOD-OF-RECORD RESULTS
56-Year Performance Comparison
[Figure 6 — Annual Peak Release Comparison]
Insert Fig 6 here: Annual peak release scatter/bar chart comparing WCM vs. FIRO across all 56 water years.
83%
Reduction in Days ≥ 150K CFS
WCM: 6 days → FIRO: 1 day
57%
Fewer Years ≥ 100K CFS Peak
WCM: 7 years → FIRO: 3 years
56-yr record peak: 274,267 CFS (WCM) vs 150,000 CFS (FIRO)

## Slide 13
RELEASE VARIABILITY
Smoother, More Predictable Releases
[Figure 7 — Release Variability Comparison]
Insert Fig 7 here: Time series or box plots showing winter release variability for WCM vs. FIRO.
Winter Release Std Dev
26%
Variability Reduction
11,482 CFS (WCM) → 8,463 CFS (FIRO)
WCM produces abrupt step changes at inflow thresholds. FIRO produces smoother, graduated releases — benefiting irrigation planning and groundwater recharge.

## Slide 14
FLOOD POOL UTILIZATION
Dynamic vs. Static Pool Management
[Figure 8 — Pool Elevation Trajectory]
Insert Fig 8 here: Reservoir elevation trace comparing WCM fixed target (848.5 ft) vs. FIRO dynamic drawdown during case study events.
WCM Target
Constant 848.5 ft regardless of forecast conditions
FIRO Target
Dynamic — down to 835.0 ft under extreme forecasts
FIRO Peak Elevation
900.4 ft across all three case studies — within 1 ft of emergency spillway

## Slide 15
KEY FINDINGS
What the Data Show
Consistent Peak Reduction
FIRO reduced peak outflows across all events and the full 56-year record
Pre-Event Drawdown Works
Creating storage before the storm is the primary performance mechanism
Safer Downstream Flows
Releases held within channel capacity; winter flows more stable and predictable
Benefits Scale with Forecast Skill
As forecast science improves, FIRO performance improves with it

## Slide 16
CONCLUSION
The Rules Need to Change — The Tools Already Exist
Limitations
At-site Oroville rules only — full system integration would yield larger benefits
Perfect foresight sets an upper bound; operational ID4A shows comparable results
What Comes Next
Oroville WCM update initiated by USACE in 2024
Same process applicable to ~750 USACE dams nationwide
The Core Argument
Decades-old static rules were designed for a climate that no longer exists. FIRO provides a scientifically grounded, operationally proven framework to close the gap between what we know and how we operate.
The science is ready. The policy window is open. Implementation is the next step.